## Slide 1: Tutorial Embedded Systems UML CODE GENERATION
Department of ElectricalEengineering and Information Technology
Welcome to the UML code generation tutorial!
In the next few hours you will learn how to generate C++ Code out of UML diagrams. This Tutorial is based on the “UML Getting Started” tutorial of the Willert company.
So, let’s start!
supported by

## Slide 2: Software
IBM® Rational® Rhapsody® for C++
With Rhapsody, we create UMLDiagrams and generate C++-code from them. The “Blinky” example will be modeled completely with the help of this environment.
KEIL MDK ARM
We need the Keil µVision IDE to flash our executable model to the target or to let it run in the built-in simulator. On top of that the IDE offers additional debugging possibilities for our model.
Realtime eXecution Framework
The Willert Embedded UML RXF™ combines Rhapsody with the Keil µVision IDE. It opzimizes the code generation for a resource friendly use in an embedded real-time enviroment.

## Slide 3: MDA Principle
Platform Independent Modell PIM
Textual Description CIM
Architectural Model
Manual Integration
Plattformspecific Model PSM
Executable Model
Transformation
Model
Plattform Description Model
Automatic Integration
UML
MCB1700/Cortex M3
Board – LEDs should
blink, no of blinking
LED showed on display
Tool: Rhapsody
Tools: Willert/Rhapsody
Tools: Keil/Willert
UML Model for blinking LEDs
On target executable C Code

## Slide 5: Codegeneration with Rhapsody in C++
UML classes generate a struct-Typ in C.
To adress components of a class (encapsulation) an automatically generated me-pointer can be used.
Example for using an attibute bitNr : Type int Attribute in a class
Usage inside a class method:
me->bitNr=16;
TODO

## Slide 6: Codegeneration with Rhapsody in C++
The name of every public operation is implicitely prefixed by the class name
To realize the ownership principle the first parameter in a class method a pointer to the owner of the method.
Example: Generated C code for class Led with operation on():void
void Led_on(struct Led * const me);
usage in implementation of blink()
...
me->BitNr++; Led_on(me); ...
The extensions are not visible in prototype / UML model
TODO

## Slide 7: Automatically generated functions
Rhapsody generates operations and objects to create, to initialize, to cleanup, and to destroy objects.
Object constructors contain creators and initializers; Objekt destructors contain cleanup and destroy operations.
  Naming:
<classname>_Create().
e.g.
B *mynewB;
mynewB = B_Create();
Object destructors delete object instances Naming: <object>_Destroy().
Available predefined types:
char char* double
float int unsigned long
long long double short unsigned
void void* unsigned short RiCString RiCBoolean OMString
TODO

## Slide 8: Object initializer
The function named init can be used to initialize attributes and links of an instance.
It is necessary to allocate the memory before (e.g. with create) Format: <object>_init()
Example: Prototype of the generated initializer for object myA of type A: void A_init(struct A* const me); (is called automatically when using create())
Primitive Operations
Primitive operations are operations defined by the modeler. They are defined by name, list of parameters and return type.
All object operations are represented in code as C-functions. Remember, first parameter is always a pointer to the owner object followed by the parameter list.
example: Method print() of object B results in:
void B_print(B* const me);
TODO

## Slide 9: Reactive Objects
Reactive Objects are objects which can receive and deal with events. Usually they are state dependent:
  They are described by a state machine or
  They have an event reception
Rhapsody automatically generates state based functions
  for entry of a state
  for consuming events
  for state request
  for leaving a state

## Slide 10: Objects
Funtcionality of classes is only usable by instances / objects
Creation of objects is done directly im Object Model Diagram or Model
Automatically generated Objects at program start are possible:
Attention: Always decide for reasonable objects, e.g. for a LED bar with 50 LEDs you should not create 50 single objects

## Slide 11: Events
Events:
enable asynchronous communication between objects and via statecharts
created inside the class which receives the event or alternatively defined as global operation
defined by using the Makro CGEN which is available in Rhapsody: CGEN( &Receiver, eventToBeSent()); e.g. CGEN( &myLED, evLEDChange());
The receiver of an event may be a global object, a local object or a subobject.
Events can transport information by using parameters. The receiver of an event can get the parameter values via
params->parametername
Note:
Creation of an event with parameters in Rhapsody: Create an operation, insert parameters, change operation type to type reception.

## Slide 12: Other useful functions
Using the IS_IN function you can decide whether an object is in a special state.
Notation: IS_IN( &object, &object_specificState)
e.g.
if(IS_IN(me, me_LEDon)) …
return value is 0 or 1 (boolean value)
Further Informations
Roundtrip means to generate a UML model out of existing code. You don‘t want to use this feature in the lab project.
Always choose „No to all“
If you are asked for roundtrip multiple times you propably have „old“ or „wrong“ elements in your model.
The path to the keil-Project is a configuration in Rhapsody. It can be changed but it is more convenient to keep it as defined.

## Slide 13: MCB1700 Board
We use a Keil MCB1700 evaluation board with a LP1768 Cortex M3 processor
To debug our Software we use the Keil Ulink2 Debugger, which allows us to debug our embedded programs on our target.
Connect the JTAG plug of the ULINK2 to the connection jack of the MCB1700
Now connect the two USB cables to ULINK2 and the 1700
Make sure that the POWER LED (red) is on
USB
USB
PC
Debugger
MCB1700

## Slide 14: MCB1700 Board
In case that Keil has problems to find the debugger after you connected it to the PC: Connect Keil with the VM (as seen in the picture below)
Usually the USB Devices are detected and connected automatically.
Use the Virtual Machine VM_SS2016_EMSYS User: Embedded Systems

## Slide 15: Blinky project GettingStarted
Let’s start IBM Rational Rhapsody Developer for C++ in the startup menu.
Off-course we could save a few pages, by omitting classes and objects in this simple Blinky. However since we will later mostly work with classes, we'd rather just put a solid foundation.
If you started IBM Rational Rhapsody
Architect for Software choose C++ as your
primary implementation language.
On the Rhapsody welcome screen of we click on the Next symbol, or choose File/New from the menu.

## Slide 16: Getting Started project
We determine an appropriate name for our project, e.g. GettingStarted in a folder in our working directory.
Yes you want to…

## Slide 17: Getting Started project
This is the user interface of Rhapsody. Please make yourself familiar with it, because this is the program we work with most of the time.
Model Browser
Diagram Area
Elementpool
for Diagrams
Debug/Output
Active Code View

## Slide 18: Getting Started project
We take a look at the model browser. Similar to the Windows Explorer, you can navigate using the (+/-) symbols through the model.
All elements of our UML model are accessible through the browser. We first start with renaming a couple of items in the model browser. The easiest way to do that is a slow double-click on the element to be renamed.
Rename

## Slide 19: Select Profiles
Chose the WST-Profile for the Willert RT-OS select File  Add Profile to Model and select the folder WST_RXF_V6.
Add both profiles.
The Profiles folder of your Project should look like this.

## Slide 20: GettingStarted project
Double-click on the MCB1700 component and select the following stereotype in the pop-up window: RXFComponent…
For the hardware specific components add the file lpc17xx.h:

## Slide 21: GettingStarted project
We open the freshly renamed OMD (Object Model Diagram) Overview by a double-click. This will open the Overview OMD in our diagram area. We draw a class in our diagram with selecting the class symbol from our element pool and name the class Led.
This class can also be found in the model browser under:
Packages / Default / Classes / Led

## Slide 22: Blinky project – Methods
Switch to the Operations-Tab and click on the New symbol and a Constructor.
Rhapsody will ask you which arguments the constructor should get. We will do that later.
Just click OK.
Add the Operations on() and off() in the same way.
Your class Led should have three operations now and look like this:

## Slide 23: Blinky project – Methods and Attributes
Next, we add two attributes to our class. The first one is bitNr, where the information which port is connected to which Led is located. The second one is delay. It’s the delay time between on and off.
Open the features of our class Led (double-click or right-click  Features) and create the two attributes at the Attributes-Tab.

## Slide 24: Blinky project – Methods and Attributes
So open the Features of the constructor Led() again and embark in the Argument tab. We create the arguments aBitNr and aDelay there, using the New symbol .

## Slide 25: Blinky project – Attributes
We have three empty methods in our class (Led() / off() / on()) and two attributes (bitNr / delay)
In order to get both variables initialized at create time we will add the following C++-code to the Implementation-Tab of the constructor Led().
What happened here?
If we later create an object of the class Led , the constructor Led() assigns a number and a delay time passed to the constructor Led() as parameters to this object.

## Slide 26: Blinky project – Attributes
In order to define one of the eight LEDs on the MCB1700 as output, we need to set the appropriate bit in the FIODIR register of the CortexM3. We do this with two code lines in the Implementation-Tab of the constructor Led(int aBitNr,int aDelay).
bitNr = aBitNr;
delay = aDelay;
LPC_GPIO1 -> FIODIR |= 0xB0000000;
// B=1011 e.g. Pin 28 and 29 with LEDs are set to output pin
// – we will not use these
LPC_GPIO2 -> FIODIR |= 0x0000007C; // LED 1,2,…5 are addressed by GPIO2,
// here all LED Pins are set to output
We have to add content to the on() and off() operation. Just fill in the lines: below.
Notes: Sauberer ist es, beim Setzen der LEDs das FIOPIN Register zu belassen. Hierfür besser verwenden: LPC_GPIO2->FIOSET |= 1<<me->bitNr; LPC_GPIO2->FIOCLR |= 1<<me->bitNr;

## Slide 27: Header and so on…
It’s time to add a header file to our “MCB1700” component. We want Rhapsody to know which specific hardware we use.
Double click on the component or open the “Features” window.
In the General tab fill in “Standard-Headers” with <lpc17xx.h>
LED.h should contain
the following include:

## Slide 28: Blinky – Statecharts
Our initializer will be automatically called at the initialization of the LED. But who will now call both our “off”- and “on”- operations?
For that we use one of the most commonly used UML diagrams - the statechart (state diagram).
In the model browser, we right click on the LED class, and wind our way through the menus.

## Slide 29: Blinky – Statecharts
Your project should look like this now:
Above our diagram area we see a tab bar in which we now see, next to our Object Model Diagram and the Welcome Screen, our newly created state chart.

## Slide 30: Blinky – State chart
We need three different elements to build our state chart from the element pool. Add two “States” and connect the two of them with one arrow (Transition) in each direction. Our chart should look like this now.
The only missing thing is an entry point now. Add it by using the “Default Transition” element.

## Slide 31: Blinky – State chart
If we want to draw the diagrams more precisely then this toolbar will support us in that:
If you select multiple objects in a diagram while keeping the Shift-Key pressed, the symbols in this toolbar will become active. Now you can align the selected objects to the edge of the diagram or to each other. The last selected object is used as pivot point!
Open the state_0 features and rename it to State_off and enter the call of the off operation at Action on entry

## Slide 32: Blinky – State chart
Enter the similar name and operation into the general tab of State_on.
In the current situation our state chart would toggle between both states. The Transitions between the states would be executed immediately.
To change that we open the features of one of the transitions with a double-click. Enter tm(me->delay)
in both transitions as “Trigger”

## Slide 33: Blinky – State chart
The tm(me->delay) uses the system clock of the CortexM3, to delay the transition for the time we specified. (We will initialize the attribute with a value later in this tutorial).
Our finished state chart should look like this:
A click on the symbol makes the “Action on entry/exit” visible in
the state icon

## Slide 34: Blinky – Instances of a class
The “LED” class is now complete.
To create an object of our “LED” class at run-time we have to initialize the class. In Rhapsody there are multiple alternatives to achieve this. The simplest possibility looks as follows:
We create a new Object-Model-Diagram to differentiate between classes and instances – to use the existing diagram would also be possible
Right click on “Object Model Diagrams”
… and call it “Runtime”

## Slide 35: Blinky – Instances of a class
Now drag the “LED” class from the model browser and drop it in the “Runtime” OMD

## Slide 36: Blinky – Instances of a class
Right click on the “LED” class in the “Runtime” LED and select:
Make an Object
At runtime an object will be created at run-time out of our
class “LED”. It is called “itsLED”.
The only thing this object is missing is a suitable “BitNr” and a value for the “Delay” in our statechart. For this we open the features of the object "itsLED“ and click the “General” tab under Initialization on the extend button.

## Slide 37: Blinky – Instances of a class
In the next window, we select the variable "aBitNr" and we click on "SetValue".
To address the LED P2.2 on the Keil MCB1700 we enter the value “2”, in the Argument Dialog under “Value”.

## Slide 38: Blinky – Instances of a class
We repeat the same game now with the argument "aDelay”. As a value we take “100” (milliseconds). To fully exploit the advantages of object orientation, we will immediately add a second instance of our class. So we will again drag the “LED” class from the browser to the “Runtime” diagram, next to the other instance, we right click the class again and from the context menu select:
Make an Object
We then click the General tab under Initialization on the Extend button and enter now for the “aBitNr” a “3” and for the
“aDelay” a “50”.

## Slide 39: Blinky – Instances of a class
That’s it!
We have just, in a very simple way, created two objects from the same class.
Both objects can be simply distinguished using the name and the attributes.
Alternative:
choose the Object template from the toolbox double click on the new object and assign Type LED.

## Slide 40: Generate / Make / RUN
We now want to generate Code and compile this code with Keil µVision
For the Keil µVision Project Willert provides a deployment. Choose Tools and select the Deploy Config entry.
There you have to insert the Path to the Keil Project. Choose the folder Code under C:\Benutzer\ADSE\Willert\Rpy_C_KeilRTX_Keil5_CM3_MCB1700_RC_V6.00\Samples\Code\GettingStarted\GettingStarted.uprojx

## Slide 41: Generate / Make / RUN
If we have made no mistakes, the model should now be able to run. To test this, we click in Rhapsody on the GMR-Button (Generate / Make / Run). It will automatically go through two steps in succession.
In the first step Rhapsody generates ANSI ‘C’-code from our diagrams and the other model components. The result of the "Generate", after you confirm the next question, can be found in:
<yourProjectDirectory>\MCB1700\Debug

## Slide 42: Generate / Make / RUN
Now start the project in the Keil µVision IDE.
C:\Users\ADSE\Willert\Rpy_C_KeilRTX_Keil5_CM3_MCB1700_RC_V6.00\Samples\Code\GettingStarted\GettingStarted.uprojx
(or in Rhapsody: choose Tools and open directly from there the Keil project)
Compile it and load your executable to your virtual device with LOAD. Start the debug mode with the debug-button to start the simulator or to debug your program.
compile download

## Slide 43: Keil µVision Development Enviroment
Of course, now we want to see if our LEDs will flash in rhythm.
We can download the program and see the blinking LED.
In case of an error or missing target, we can use the Keil Simulator: We have to activate the debug mode of the Keil IDE.
When we are in debug mode, an IO-window automatically opens or we choose the General Purpose IO Fast Interface and Select GPIO2. There we can monitor the state of the ports.
If we now click on the RUN button, we can see how bit “2” of FIO2SET toggles in the 100ms rhythm and bit “3” in 50ms intervals.
We can switch from Simulator to Hardware with Project/OptionsforTarget

## Slide 44: Laboratory Guide – Embedded Systems Prof. M. von Schwerin Prof. N. Normann On the next few pages several tasks and exercises are described which have to be solved during the laboratory.
Department of Electrical Engineering and Information Technology
Notes: Anmerkungen:
Komposition mir Multiplizität 1 funktioniert nur, wenn Init() der Komponente keine Parameter hat (Standardkonstruktor wird automatisch verwendet)
Kaskadierung funktioniert nur zur direkt benachbarten Klasse hin:
itsBoard->itsLED.on() wird muss in C-Code so geschrieben werden:
LED_on(me->itsLED)

## Slide 45: Annotations
Start the exercise part with a new project. Do not use parameters for the initialization of a class because in the following we will also use other types of instantiation of an object as shown in the example.
Create a new project for every exercise.
Therefore you can select a suitable already existing project (Hint: Note that the last project is not always the best fit for the next exercise)
You should copy selected former project by using “save as” and create a new top directory folder.

## Slide 46: Exercise 1
Modify the project from the tutorial, that
  a) all LED’s (P2.2 to P2.6) flash in turn and go out in reverse order.
  b) all LED’s flash in a row to build a ‘moving light’.
Modify the time, which the “moving light” takes for one iteration. Therefore implement a code that changes the “Delay” variable dynamically during the runtime.
Exercise 2

## Slide 47: Exercise 3
Now the iteration time should be modified by using the Poti, which is right beside the LEDs. Its potential is connected via jumper AD0.2 to the A/D Converter channel 2 of the LPC1768. The potentiometer changes should be processed using polling mode.
Hint: For the configuration of the A/D Converter the following code can be used.
  AD Initialization:
  LPC_PINCON->PINSEL1 &= ~(3<<18);/*P0.25 is GPIO */
  LPC_PINCON->PINSEL1 |= (1<<18);/*P0.25 is AD0.2 */
  LPC_SC->PCONP |= (1<<12);/*Enable power ADC block */
  LPC_ADC->ADCR = (1<< 2) | /*select AD0.2 pin */
  (4<< 8) | /*ADC clock is 25MHz/5 */
  (1<<21); /* enable ADC */

## Slide 48: Exercise 3 continue
  Sampling:
  LPC_ADC->ADCR |= 0x01200000; /*Start A/D Conversion*/
  do{
  val= LPC_ADC->ADDR2; /*Read A/D Data Register into val*/
  }while((LPC_ADC->ADGDR & 0x80000000) == 0); /*Wait for end of A/D Conversion */
  LPC_ADC->ADCR &= ~0x01000000; /*Stop A/D Conversion*/
  val= (val >> 8) & 0x03FF; /* Extract value Conversion*/
  Exercises 1 – 3 have to be checked through a lab advisor. Please mail your projects and submit printouts of your implementations, methods and state charts to the advisors.

## Slide 49: Exercise 4
The LEDs should now be controlled by a new class “Board“. This class sends suitable events to the LED instances to change from “on“ to “off“ state. Try to use reasonable UML relations in your class diagram. The delay does not have to be controlled by the Poti in this exercise.
Hint:
  Events can be used for asynchronous communication between objects beyond the borders of their state charts. An event is created as an operation of the class that receives the event or as an global operation. The predefined macro CGEN defines an event
      CGEN( &Receiver, sendEvent());
  Parameters can be passed to events similar to functions and so it is possible to transport informations. The receiver can access the parameters via
      params->parametername
  Attention: Create an event with parameters as “Operation” and add its parameter. After that, change the Stereotype of the operation to “Reception”.

## Slide 50: Exercise 5
Print now the number of the currently flashing LEDs onto the LCD Display.
Hint: The display requires additional drivers which are provided by the Keil IDE. In the Rhapsody project you should add two additional headers: GLCD_config.h, Board_GLCD.h In Keil choose theManage Run Time Envronment and add
  Board Support – Graphic LCD
  CMSIS Driver – SPI – SSP
  Device – Seclect all

## Slide 51: Exercise 5 (continued)
  You now see the Board Support and CMSIS in your project
  Choos Device – RTE_Device.h and select SSP1
  Save the settings and close the project
  Now you can use the GLCD commands in your Rhapsody Project

## Slide 52: Exercise 5 continued
  You can use the following commands for controlling the display:
  extern GLCD_FONT GLCD_Font_16x24; //in case you don’t want to
  // use the default string
  GLCD_Initialize(); GLCD_SetBackgroundColor(GLCD_COLOR_WHITE);
  GLCD_SetForegroundColor(GLCD_COLOR_BLUE);
  GLCD_SetFont(&GLCD_Font_16x24);
  GLCD_ClearScreen();
  GLCD_DrawString(2,3,”Hello”); //line,column, text as char-Array GLCD_Bargraph(unsigned int x, unsigned int y, unsigned int w, unsigned int h, unsigned int val);
    /*Print a Value val as bargraph to line x and column y with the pixel width w and high h* Annotation: in C sprintf(str, "i is %i", i) changes integer i to a C string str (char array) with the same content ( header stdio.h necessary)

## Slide 53: Exercise 6
Model a periodic A/D conversion of the potentiometer voltage. The interval between two AD samples should be 10 ms. Convert the AD values to a number between 0 to 100. Print the current value to the LCD as number and bargraph.
Design a complete LED supervision through the board class. The delay of the “moving-light“ should be controlled through the potentiometer in the area 0 to 100.
Hint: Consider again how to use the UML relations reasonably.
  Exercises 4 – 7 have to be checked through a lab advisor. Please mail your projects and submit printouts of your implementations, methods and state charts to the advisors.
Exercise 7

## Slide 54: Exercise 8
Use the “joystick“ on the MCB1700 board to control the „moving light“ through user inputs. Model a LED supervision that allows the user to enable/disable, stop and restart the LED line by using the joystick. The joystick should be prompted by polling.
Hints:
  Joystick initialization: LPC_GPIO1->FIODIR&= ~((1UL<<20)|(1UL<<23)| 1UL<<24)| (1UL<<25)| (1UL<<26)); /* Port P1.20, 1.23.26 is input (Joystick)*/
  The joystick position can be identified with: position = (LPC_GPIO1->FIOPIN >> 20) & Joystick_Mask ; // last 7 Bits now are related to Joystick
  Bit 4 to 7 includes the information about the joystick position: position = position >> 3;

## Slide 55: Exercise 8 continue
  Joystick_Mask is a “constant“. A constant can be created as a “Type“ through a right click on the “Default“ package and selecting “Add New / Type“. Call the new type MASK and write to “Declaration”: #define Joystick_Mask 0x79
We need another constant DIRECTION from kind “Enumeration“ which looks like:
The variable “position“ can now be compared with the DIRECTION items.

## Slide 56: Exercise 9
Now use the EINT0 Interrupt (triggered through button INT0) to start and stop the LED line.
Hint:
  The EINT0 interrupt gets initialized through following code: LPC_PINCON->PINSEL4 |= (1<<20); /* Port 2.10 is EINT0 */ LPC_SC->EXTMODE |= (1<<0); /* EINT0 is edge sensitive */ LPC_SC->EXTPOLAR &= ~(1<<0); /* EINT0 is falling edge sensitive */ NVIC_EnableIRQ(EINT0_IRQn); /*Enable IRQ interrupt for INT0 in NVIC */
  An operation IRQHandler() is necessary. The core interrupt handler jumps to this function. There the EINT0 Interrupt Service Routine (ISR) code takes place. In the ISR first clear the pending EINT0 interrupt flag: LPC_SC->EXTINT |= (1<<0); /* clear EINT0 interrupt */

## Slide 57: Exercise 10 (optional) Ethernet
We now want to use the Ethernet communications which ist provided by our board. We need an additional platform model file and an idea how to model a class Ethernet. Therefore there is a starting project in E:Ethernet_Aufgabe. Use this as start and deploy the Keil Project to E:Ethernet_Aufgabe\GettingStarted_Ethernet\ GettingStarted
Now develop a model which uses two boards. Connect them with an Ethernet cable. Then model the following scenario: If you push the joystick up on one board, the other board shows an LED light. If you push the joystick down, the light switches off again. For the communication between the boards Ethernet is used.

## Slide 58: Blinky Test
1. Open Rational Rhapsody
2. Choose Blinky Example Project in Rhapsody
C:\users\Embedded Systems\IBM\Rhapsody\7.6.1\Share\WST_RXF_V5\
LisztV5.5r9\Smples\Model\Blinky.rpy
3. Generate Code
4. Open Keil µVision
5. Choose Target Release ( Compile Project not necessary)
7. Download on target LED is blinking